## Slide 1: Embedded Machine Learning
Using STM32CubeIDE and X-CUBE-AI Extension.
for model integration and code generation.
Deploying a Pretrained Text Classification Keras Model.
optimized for embedded systems and validated on the STM32 NUCLEO-H723ZG board
Achieving Inference Parity with Python
by comparing outputs between the STM32 and Python runtime environments using predefined inputs .
Notes: Using STM32CubeIDE and X-CUBE-AI Extension:
Integrating a pretrained Keras model with STM32 microcontrollers using the STM32CubeIDE and the X-CUBE-AI extension.
Deploying a Pretrained Text Classification Keras Model:
Implementing a modified Dense-only Keras model for text classification, optimized for use on the STM32 NUCLEO-H723ZG board.
Achieving Inference Parity with Python:
Ensuring inference results on the STM32 match those of the original Python implementation, validating model consistency across platforms.

## Slide 2: Creating the STM32 Project
Launch New STMCubeIDE or CubeMX Project
Software Updates for X-CUBE-AI
Select Board, Generate New Project
Accept Defaults
Increase Stack and Heap
Select X-CUBE-AI from Middleware
Notes: Show the board statistics once selected
The NUCLEO-H723ZG was chosen for
Microcontroller: STM32H723ZGTx
Core: ARM Cortex-M7 (32-bit, up to 550 MHz) with double-precision FPU (Floating Point Unit) and DSP (Digital Signal Processing) instructions.
Memory:
Flash Memory: 1 MB
RAM: 564 KB distributed ram
Once the board is selected, go the project view and increase heap and stack. Stack0x2000, heap 0x4000

## Slide 3: Importing the “Dense” Model
Go the Middleware, select X-CUBE-AI
Click + network
  Browse to text_classification_dense_input.h5
Run “Analyze”
Save the .ios or “Save All”
Yes to save, yes to generate code.
Notes: Why “Embedding” Layer Wasn’t Supported:
The Embedding layer maps each word in a vocabulary to a dense vector representation, typically using a lookup table. It requires a large memory footprint to store embeddings, which can be problematic for microcontrollers with limited RAM and Flash.
STM32’s X-CUBE-AI framework doesn’t support Embedding layers because they don’t translate well to a fixed architecture where memory access and size constraints are crucial.
Solution: Dense-Only Model: The Dense model eliminates the Embedding layer and instead uses preprocessed float values (e.g., 0.8, 0.5, 0.2) as direct inputs to represent the sentiment of each example. The inputs are mapped directly to the first Dense layer, which performs a linear transformation to capture relationships between these values and the model’s output.
This approach simplifies memory management and reduces the model’s complexity, making it suitable for deployment on the STM32 microcontroller.
Key Difference: The original model used embeddings to capture semantic relationships between words, while the Dense model relies on numerical inputs that directly represent sentiment. This makes the Dense model more efficient and compatible with the limited hardware resources of the microcontroller.
Tip: restart the CubeIDE to flush the filebuffer so it doesn’t keep prompting you.

## Slide 4: Build, Configure UART for Printing
Optional Analyzing on Desktop, Target
Make sure you add clock init (see MX_USART3_UART_Init)
__HAL_RCC_USART3_CLK_ENABLE();
Sync settings with Virtual COM Port in Device Manager
Same with serial terminal reader (Terminal, putty, etc.)
Compare both to MX_USART3_UART_Init settings
Project Properties, C/C++ Build Settings
  mcu/mpu settings, use float with printf with nano-newlib
Notes: Reminder: If using my project files, the UART configuration should be ready to use without changes.
These steps are only necessary if starting from scratch or creating a new project.
Ensure your serial terminal reader (e.g., Terminal, Putty) matches these UART settings:
Baud rate (e.g., 115200)
Data bits (e.g., 8)
Stop bits (e.g., 1)
Parity (e.g., None)
Flow control (e.g., None)
Configure Project Properties in STM32CubeIDE:
C/C++ Build Settings:
Go to Project -> Properties -> C/C++ Build -> Settings.
MCU/MPU Settings:
Ensure Use float with printf is enabled.
Select nano-newlib for lightweight library settings.
This ensures smooth printing of floating-point values via UART with minimal memory overhead.

## Slide 5: X-CUBE-AI Generated Code and Reports
Project Explorer, X-CUBE-AI, App
network_generate_report.txt
Note in the report, output dir, verbose model format
app_x-cube-ai.c network.c network_config.h network_data.h network_data_params.h
app_x-cube-ai.h network.h network_data.c network_data_params.c network_generate_report.txt
Doxygen view of the network framework codegen next
Notes: Show network report.txt, show output.cvs, json
Show USER TODO Code
Show doxygen next slide

## Slide 6: X-CUBE-AI CodeGen: What the Network framework “Does”
Doxygen view and X-CUBE-AI-Framework.pdf under X-CUBE-AI/App
Initializes the AI Network: Sets up network parameters, input and output shapes, and loads weights for inference.
Manages Memory Buffers: Allocates and deallocates memory for model inputs, outputs, and intermediate layers.
Handles Model Inference: Executes the neural network by feeding inputs through layers to generate predictions.
Configures Data I/O: Prepares data in the correct format for the model and retrieves outputs for further processing.
Provides Debug and Profiling Support: Includes hooks for performance monitoring and debugging of inference runs.
Notes: Read from the pdf, maybe even show it, it will be checked in.

## Slide 7: Pre-Processing Step with Python
Run Python Script: Execute the run_inference.py to generate preprocessed float values for each text example.
Observe Output and Mappings: Display the preprocessed values and compare them with the expected sentiment scores.
Explain Simplified Vocabulary: Highlight that the vocabulary is manually defined and simpler than the original TensorFlow tutorial.
No TensorFlow Tokenizer in Embedded Code: Due to resource constraints, the full TensorFlow tokenizer can’t be used directly in STM32.
Use Python for Input Floats: Python is used to map text inputs to float values, which are then fed directly into the model on STM32.
Notes: Read the X-CUBE-AI-Python-Parity.pdf

## Slide 8: Editing the “USER CODE”
Limited to one input/output at a time per AI_NETWORK_IN_NUM, AI_NETWORK_OUT_NUM, both defined as “1” dimension
Grab the float “indices” and create an array, e.g.
  const float predefined_inputs[] = {0.8f, 0.5f, 0.2f};
  Edit int acquire_and_process_data(ai_i8* data[])
  Edit int post_process(ai_i8* data[])
  Review X-CUBE-AI/App/app_x-cube-ai.c
Notes: Read the Editing_USER_CODE.pdf

## Slide 9: Build, Run
Build, Debug
Breakpoint in post_process
Setup Terminal

## Slide 10: Recap
Create New Project in STM32CubeIDE
Select NUCLEO-H723ZG board and enable X-CUBE-AI middleware.
Import the Dense Model (text_classification_dense_input.h5)
Navigate to the X-CUBE-AI tab, create a new network, and select the model file.
Analyze and Generate Code
Run the analysis to verify compatibility, save configuration, and generate the necessary code files.
Configure Project Properties and UART
Increase stack and heap size.
Set up UART for serial printing.

## Slide 11: Recap (cont.)
Run Python Script for Preprocessing
Use run_inference.py to map text inputs to float values.
Simplified Vocabulary and Indices
Predefined float values (0.8, 0.5, 0.2) used instead of TensorFlow tokenizer.
Mapping Floats to Sentiments
0.8 → Positive sentiment
0.5 → Neutral sentiment
0.2 → Negative sentiment

## Slide 12: Contribute
Please provide feedback in the form of Issues
https://github.com/stevemac321/EmbeddedMachineLearning
Links in the description of the Video